Twist Throttle Cable with 48 Volt LED Meter

This hall effect twist throttle fits most Chinese made electric scooters. 

Fits standard 7/8" OD handlebars and cable is approximately 50" long with four push-in connectors. 

Throttle has 3 LED indicator lights. One LED is for power status and the other two LED indicator lights are for battery status.

Wiring Diagram

| Throttle |  | Controller | Description |
| --- | --- | --- | --- |
| Red | connects to | Red | Voltage 4.3 to 5.0 Volts |
| Black | connects to | Black or Yellow | Ground |
| Green | connects to | Green, Blue or White | Speed Adjusting Signal (0 to 5 Volts) |
| Yellow | connects to | Orange or Yellow | LED Battery Status Meter (+ 48 Volts) |